## Slide 2: Time-predictable End-system Design for Real-Time Communication
Eleftherios Kyriakakis

## Slide 3: Outline
Introduction
  Cyber-physical systems
  Motivation
Background
  Time-predictable hardware
  Task execution
  Real-time communication
  Time synchronization
Contributions
  Hardware-assisted clock synchronization with PTP
  Fault-tolerant PTP synchronization using multi-domain aggregation
  Time-predictable open-source TTEthernet end-system
  Synchronizing real-time tasks in time-triggered networks
  Evaluation the runtime system by distributing a flight controller
Conclusion
  Composing a time-triggered system
  Future Outlook

## Slide 4: Introduction Cyber-physical systems
Computing systems have evolved
From Information processing devices,
Industrial, Automotive & Aerospace
BMW and Audi motors triplicated the number of electronic control units in their vehicles since 1995.
Airbus and Boeing has recently introduced Ethernet-based communication protocols in modern aircraft.
Nowadays
Distributed embedded systems interface with multiple sensors to control various actuation systems.
Cyber-physical systems networks.
To embedded microcontrollers in several control systems.
Hard real-time systems
Embedded systems in safety-critical domains.
Functional requirement of timeliness and in-order data reception without losses.

## Slide 5: Introduction Example cyber-physical system network
Research contributions mapped to the individual components of the real-time end-systems.
Components:
  Network protocol provides the communication channel.
  Time synchronization coordinates the data flow.
  Runtime system interfaces with sensors and actuators.
  Cyclic scheduling coordinates the task execution.
Goal:
  Compose a time-predictable end-system for real-time communication.
  Develop hardware/software components for time-predictable communication & computation.

## Slide 6: Introduction Motivation
Hard real-time systems require:
  End-to-end timing analysis
  Task scheduling
  Precise time-synchronization
  Quality-of-control
Current research:
  Significant optimization on the components individually.
  Use of proprietary network interface cards.
  Focus on simulation and analysis.
  Reliability for PTP needs more research.
This research work goals:
  Investigate the composition of a time-predictable end-system.
  Provide open-source solutions for time-triggered communication.
  Investigate end-to-end isochronous computation and communication.
  Provide fault-tolerant PTP synchronization.

## Slide 7: Background Hard real-time systems
The functional correctness depends both on their functional aspects on their temporal behavior.
Different temporal requirements classify real-time systems into three classes:
  Soft real-time, i.e., a streaming media application.
  Firm real-time, i.e., motor controllers and some actuation devices.
  Hard real-time, i.e., a vehicle airbag system, aircraft landing gears etc.
Variations in the system input can lead to different computation/communication times.
Time-predictable architecture has to guarantee bounded:
  worst-case execution time (WCET): for computation.
  worst-case end-to-end latency (WCEL): for communication.

## Slide 8: Background Task execution

## Slide 9: Background Task execution

## Slide 10: Background Real-time Communication

## Slide 11: Background Real-time Communication - ET

## Slide 12: Background Real-time Communication - RC

## Slide 13: Background Real-time Communication - TT

## Slide 14: Background Time synchronization

## Slide 15: Background Time synchronization